## Slide 1
Design & Implementation of a
5-Stage Pipelined RV32I Processor
RISC-V Base Integer Instruction Set in Verilog HDL
Adesh Pandey
079BEI004
Aayush Gelal
079BEI002
Bishesh Paudel
079BEI016
Tribhuvan University · Institute of Engineering · Pulchowk Campus
Department of Electronics & Computer Engineering · March 2026

## Slide 2
INTRODUCTION
Why RISC-V? Why Pipelining?
RISC-V: The Open Standard ISA
• Open & free: no licensing fees, unlike ARM or x86
• Modular design: base integer set (RV32I) + optional extensions
• Industry adoption: SiFive, Google, NVIDIA, Qualcomm
• Academic standard: clean ISA ideal for teaching architecture
Why Pipelining?
• Throughput boost: overlap execution of multiple instructions
• Higher clock speed: shorter critical path per stage
• Real-world relevance: all modern CPUs are pipelined
Project Objectives
• Implement full RV32I base instruction set (37 instructions)
• Build a 5-stage pipeline with forwarding & hazard detection
• Evolve from single-cycle → pipelined architecture
• Add performance counters for quantitative analysis
• Benchmark with real programs and compare CPI
• Extend ISA with custom crypto instruction (ROL)
• Verify with comprehensive testbenches
Key Insight: A 5-stage pipeline achieves ~4.4x throughput over single-cycle, despite ~14% CPI penalty. Custom ROL gives 1.35x crypto speedup.

## Slide 3
INSTRUCTION SET
RV32I Base Integer Instructions
37 Instructions Implemented
R-Type (Register-Register) — 10 instructions
ADD SUB SLL SLT SLTU XOR SRL SRA OR AND
I-Type (Immediate) — 9 instructions
ADDI SLTI SLTIU XORI ORI ANDI SLLI SRLI SRAI
Load / Store — 2 instructions
LW SW
Branch, Jump & Upper Immediate
B-Type (Branch) — 6 instructions
BEQ BNE BLT BGE BLTU BGEU
J-Type (Jump) — 2 instructions
JAL JALR
U-Type (Upper Immediate) — 2 instructions
LUI AUIPC
Instruction Format Encoding
31 25 24 20 19 15 14 12 11 7 6 0
R: [ funct7 ] [ rs2 ] [ rs1 ] [f3 ] [ rd ] [opcode ] <- ADD, SUB ...
I: [ imm[11:0] ] [ rs1 ] [f3 ] [ rd ] [opcode ] <- ADDI, LW
S: [ imm[11:5]] [ rs2 ] [ rs1 ] [f3 ] [imm4:0 ] [opcode ] <- SW
B: [imm[12|10:5]] [rs2 ] [ rs1 ] [f3 ] [im4:1|11][opcode ] <- BEQ, BNE
U: [ imm[31:12] ] [ rd ] [opcode ] <- LUI, AUIPC
J: [imm[20|10:1|11|19:12] ] [ rd ] [opcode ] <- JAL

## Slide 4
ARCHITECTURE
Single-Cycle Baseline
How Single-Cycle Works
• Each instruction completes in one clock cycle
• All hardware used sequentially in one cycle
• Clock period = longest instruction delay path
• CPI is always 1.0 by definition
The Problem
Critical path bottleneck: The clock must be slow enough for the slowest instruction (LW: PC → IMEM → RegFile → ALU → DMEM → Mux). Every instruction pays this penalty.
Single-Cycle Datapath
PC
IMEM
RegFile
ALU
DMEM
T_critical = T_pc + T_imem + T_reg + T_alu + T_dmem + T_mux
Key Insight: In single-cycle, a simple ADD takes the same time as the slowest LW instruction. Pipelining breaks this into 5 shorter stages, allowing ~5x higher clock frequency.

## Slide 5
ARCHITECTURE
5-Stage Pipeline Architecture
IF
Instruction Fetch
ID
Instruction Decode
EX
Execute / Branch
MEM
Memory Access
WB
Write Back
IF/ID
ID/EX
EX/MEM
MEM/WB
Stage | Operations | Key Modules
IF | Fetch instruction at PC, compute PC+4 | pc, imem, pc_adder
ID | Decode opcode, read registers, gen immediate | control, regfile, imm_gen
EX | ALU operation, branch decision, target calc | alu, forwarding mux
MEM | Load/Store data memory access | dmem
WB | Select result and write to register file | result mux, regfile
Register | Width | Key Fields
IF/ID | ~67 bits | instruction, PC, PC+4
ID/EX | ~180 bits | controls, rd1, rd2, imm, rs1/rs2/rd
EX/MEM | ~103 bits | ALU result, write data, rd, controls
MEM/WB | ~104 bits | ALU result, mem data, rd, controls
Key advantage: Each stage is 1/5 of the critical path -> clock runs ~5x faster.

## Slide 6
ARCHITECTURE
Pipeline Timing & Instruction Overlap
Ideal Pipeline Execution (No Hazards)
Multiple instructions execute simultaneously, each in a different stage:
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9
Instr 1 | IF | ID | EX | MEM | WB |  |  |  | 
Instr 2 |  | IF | ID | EX | MEM | WB |  |  | 
Instr 3 |  |  | IF | ID | EX | MEM | WB |  | 
Instr 4 |  |  |  | IF | ID | EX | MEM | WB | 
Instr 5 |  |  |  |  | IF | ID | EX | MEM | WB
Throughput Comparison
Single-Cycle: 1x throughput
5-Stage (ideal CPI=1): 5x throughput
5-Stage (real CPI=1.14): ~4.4x throughput
Why Not Perfect 5x?
• Data hazards: instruction depends on unavailable result
• Control hazards: branch decision not known until EX
• Pipeline fill/drain: startup & shutdown overhead
Speedup = N / CPI = 5 / 1.14 = 4.39x

## Slide 7
DESIGN
Hardware Module Breakdown
pc.v
32-bit program counter with reset & enable for stall control
16 lines
pc_adder.v
Simple combinational adder: PC + 4
7 lines
imem.v
64-word instruction memory. NOP-initialized. Loads .hex
15 lines
control.v
Combinational decoder: opcode+funct3+funct7 → 10 control signals
133 lines
regfile.v
32x32 register file. x0=0. Write-through bypass for WB→ID
24 lines
imm_gen.v
Sign-extended immediates for all 6 instruction formats
33 lines
alu.v
11-operation ALU: ADD,SUB,AND,OR,XOR,SLT,SLTU,SLL,SRL,SRA,ROL
28 lines
dmem.v
64-word data memory. Async read, sync write
18 lines
top.v
Pipeline: 4 pipe regs, forwarding, hazard detect, perf counters
401 lines
Total: 9 modules · 675 lines of Verilog · 5 testbenches · 227 lines of test code

## Slide 8
HAZARDS
Pipeline Hazards Overview
Data Hazards (RAW)
Instruction needs a register value not yet written back.
ADD x1, x2, x3 // writes x1
SUB x4, x1, x5 // reads x1!
Solution: Data forwarding + load-use stall
Control Hazards
Branch outcome unknown until EX — wrong instructions may enter pipeline.
BEQ x1, x2, target
// next 2 instrs fetched
// must flush if taken
Solution: Pipeline flush (2-cycle penalty)
Load-Use Hazard
Load result only available after MEM, but next instruction needs it in EX.
LW x6, 0(x0) // data at MEM
ADDI x7, x6, 1 // needs in EX!
Solution: 1-cycle stall + MEM/WB forward
Hazard Type | Resolution | Penalty
RAW (1-gap) | Forward from EX/MEM | 0 cycles
RAW (2-gap) | Forward from MEM/WB | 0 cycles
RAW (3-gap) | Register write-through | 0 cycles
Load-Use | Stall 1 cycle + forward | 1 cycle
Branch taken | Flush IF/ID + ID/EX | 2 cycles
4 out of 5 hazard types resolved with ZERO penalty thanks to forwarding. Only load-use requires 1-cycle stall, and branches cost 2 cycles when taken.

## Slide 9
HAZARDS
Data Forwarding Unit
Forwarding Paths
ID
EX
MEM
WB
FWD MUX
← EX/MEM Forward (1-gap, 0 penalty)
← MEM/WB Forward (2-gap, 0 penalty)
Forwarding Control Logic
// Forward A (ALU src1)
assign forward_a =
// EX/MEM hazard (1-gap)
(ex_mem_reg_write && ex_mem_rd != 0
&& ex_mem_rd == id_ex_rs1) ? 2'b10 :
// MEM/WB hazard (2-gap)
(mem_wb_reg_write && mem_wb_rd != 0
&& mem_wb_rd == id_ex_rs1) ? 2'b01 :
2'b00; // No hazard
Write-Through Bypass (3-gap Bug Fix)
// In regfile.v - handles WB->ID same cycle
assign rd1 =
(a1 == 0) ? 32'b0 :
(we3 && a3 == a1 && a3 != 5'b0) ? wd3 :
rf[a1];
Bug fix: without this, 3-instruction gap reads stale data.
Forwarding eliminates 100% of data stalls on Fibonacci benchmark. Every RAW dependency resolved with zero penalty.

## Slide 10
HAZARDS
Load-Use Stalls & Branch Flushes
Load-Use Stall Mechanism
// Detect load-use hazard
wire load_use_hazard =
id_ex_result_src == 2'b01 // load in EX
&& (id_ex_rd == if_id_rs1
|| id_ex_rd == if_id_rs2)
&& id_ex_rd != 0;
// Stall action:
// 1. Freeze PC (don't fetch next)
// 2. Hold IF/ID (re-decode same instr)
// 3. Insert NOP in ID/EX (bubble)
Branch Flush Mechanism
// Branch resolved in EX stage
wire branch_taken =
(id_ex_branch && alu_zero) // BEQ
|| id_ex_jump // JAL
|| id_ex_jalr; // JALR
wire flush = branch_taken;
// Flush action:
// 1. Zero out IF/ID register (NOP)
// 2. Zero out ID/EX register (NOP)
// 3. Redirect PC to branch target
Stall Timing
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
LW x6,0(x0) | IF | ID | EX | MEM | WB |  | 
ADDI x7,x6,1 |  | IF | ID | stall | EX | MEM | WB
Flush Timing
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
BEQ x1,x2,T | IF | ID | EX | MEM | WB |  | 
PC+4 (wrong) |  | IF | flush |  |  |  | 
Target instr |  |  |  | IF | ID | EX | MEM
After stall, data forwarded from MEM/WB to EX (cost: 1 cycle)
2 wasted cycles per taken branch (fetched instructions are flushed)

## Slide 11
INSTRUMENTATION
Performance Counters & Halt Detection
Counter | What It Measures | How
perf_cycles | Total clock cycles elapsed | Increments every posedge clk
perf_instrs | Retired (completed) instructions | Counts when mem_wb_valid == 1
perf_stalls | Load-use hazard stall cycles | Counts when stall signal asserted
perf_flushes | Branch/jump flush events | Counts when flush signal asserted
Derived Metrics
CPI = perf_cycles / perf_instrs
Stall Rate = perf_stalls / perf_cycles x 100%
Flush Rate = perf_flushes / perf_cycles x 100%
Speedup = N / CPI (vs single-cycle)
Valid Bit Propagation
// Valid bit pipeline
reg id_ex_valid, ex_mem_valid,
mem_wb_valid;
// Count only when instr reaches WB
if (mem_wb_valid && !halted)
perf_instrs <= perf_instrs + 1;
Halt Detection
// Detect jal x0, 0 (self-loop)
wire halt_instr =
opcode == JAL && rd == x0
&& offset == 0;
// Freezes all counters on halt
Programs end with "jal x0, 0" to halt cleanly. Counters freeze so results reflect only program execution, not idle time.

## Slide 12
TESTING
Benchmark Programs & Verification
Fibonacci Benchmark (benchmark.hex)
Iterative computation of F(0)...F(9), stores all 10 values to data memory.
a=0; b=1; mem[0]=a; mem[4]=b;
for (i=2; i<10; i++) {
temp = a + b;
mem[i*4] = temp;
a = b; b = temp;
}
halt; // jal x0, 0
Address | Value | Fib
mem[0] | 0 | F(0)
mem[1] | 1 | F(1)
mem[2] | 1 | F(2)
mem[3] | 2 | F(3)
mem[4] | 3 | F(4)
mem[5] | 5 | F(5)
mem[6] | 8 | F(6)
mem[7] | 13 | F(7)
mem[8] | 21 | F(8)
mem[9] | 34 | F(9)
Pipeline Hazard Test (program.hex)
Test | Scenario | Result
1 | EX/MEM forwarding (back-to-back) | PASS
2 | MEM/WB forwarding (2-gap) | PASS
3 | Load-use hazard (stall+fwd) | PASS
4 | R-type forwarding chain | PASS
5 | Store with forwarded data | PASS
6 | Branch with forwarding | PASS
Unit Tests
Testbench | Tests | Status
alu_tb.v | ADD, AND, SUB + zero flag | PASS
regfile_tb.v | Write, read, x0 hardwired | PASS
top_tb.v | Full pipeline (35 instrs) | PASS
benchmark_tb.v | Fibonacci (64 instrs) | PASS
crypto_tb.v | ChaCha20 SW vs HW | PASS
Exercises: back-to-back deps, forwarding paths, branches, memory ops.

## Slide 13
RESULTS
Performance Results
1.14
CPI (Fibonacci)
0
Stall Cycles
9.9%
Flush Overhead
4.4x
Throughput Gain
Metric | Single-Cycle | 5-Stage Pipeline
Clock Cycles | 71 | 81
Instructions Retired | 71 | 71
CPI | 1.00 | 1.14
Stall Cycles | 0 | 0
Flush Cycles | 0 | 8
Flush Rate | 0% | 9.9%
Max Clock Freq | 1/Tcrit | ~5/Tcrit
Effective Throughput | 1x | ~4.4x
Metric | Value
Clock Cycles | 60
Instructions Retired | 55
CPI | 1.09
Stall Cycles | 1
Flush Cycles | 1
Stall Rate | 1.67%
Flush Rate | 1.67%
Even with deliberate hazard-heavy code, CPI stays at 1.09 thanks to the forwarding unit.

## Slide 14
ANALYSIS
Quantitative Analysis & Comparison
CPI Breakdown — Fibonacci
Component | Contribution to CPI
Base CPI (ideal pipeline) | +1.000
Load-use stall penalty | +0.000
Branch flush penalty | +0.113
Pipeline fill/drain | +0.028
Measured CPI | 1.141
Cycle Breakdown — Fibonacci (81 cycles)
Useful work: 71 cycles (87.7%)
Branch flushes: 8 cycles ( 9.9%)
Pipeline fill/drain: 2 cycles ( 2.5%)
Load-use stalls: 0 cycles ( 0.0%)
Forwarding Effectiveness
With forwarding: CPI = 1.14
Without forwarding: CPI = 1.6 - 2.0 (est.)
Forwarding eliminates 100% of data stalls on Fibonacci. Every RAW dependency resolved by EX/MEM, MEM/WB, or write-through with zero penalty.
Architecture | Clock Period | CPI | Throughput
Single-Cycle | Tcrit | 1.00 | 1/Tcrit
Pipeline (ours) | Tcrit/5 | 1.14 | 4.39/Tcrit
Pipeline (no fwd) | Tcrit/5 | ~1.8 | ~2.78/Tcrit
Throughput = IPC x f_clk = (1/1.14) x 5f = 4.39f Speedup: 4.39x over single-cycle | Efficiency: 87.7%

## Slide 15
ISA EXTENSION
Custom ROL Instruction — ChaCha20 Quarter-Round
What is ChaCha20?
• Stream cipher: used in TLS 1.3, WireGuard, SSH, Android encryption
• Core op: quarter-round — built from ADD, XOR, Rotate-Left
• Standard RV32I has no rotate — emulate with 3 instructions
• RISC-V Zbkb extension adds ROL/ROR for this reason
Our Custom Instruction
// Added to alu.v
4'b1010: result =
(src1 << src2[4:0]) |
(src1 >> (32 - src2[4:0])); // ROL
// control.v: custom-0 opcode (0001011)
// R-type format, uses existing pipeline
ChaCha20 Quarter-Round Algorithm
// Input: a=0x61 b=0x62 c=0x63 d=0x64
// Repeat 4 rounds of:
a += b; d ^= a; d <<<= 16;
c += d; b ^= c; b <<<= 12;
a += b; d ^= a; d <<<= 8;
c += d; b ^= c; b <<<= 7;
Round-by-Round Trace
 | a | b | c | d
Input | 00000061 | 00000062 | 00000063 | 00000064
Round 1 | 700010CD | DBEEECEB | A7B7CDD3 | A710CD70
Round 2 | 31529DEE | C935724B | 72F1CAD2 | 9A711001
Round 3 | F0201BDA | 1EA20D3F | 8BA54FBB | 187B23F0
Round 4 | D576E19B | 1898E8F8 | 36858953 | 9FF722DF
Standard RV32I (3 instrs):
SLLI x5, x4, 16 // d<<16
SRLI x6, x4, 16 // d>>16
OR x4, x5, x6 // combine
With Custom ROL (1 instr):
ROL x4, x4, x12 // done!
// x12 holds 16
// 1 instruction, 1 cycle
Both versions produce identical output — verified in simulation.

## Slide 16
ISA EXTENSION
Crypto Benchmark: Software vs Hardware — Results
1.35x
Speedup
26%
Fewer Cycles
28
Instrs Saved
36%
Code Reduction
Metric | Software (RV32I) | Hardware (+ROL) | Delta
Clock Cycles | 107 | 79 | -28 (26%)
Instructions Retired | 101 | 73 | -28 (28%)
Loop Body Size | 22 instrs | 14 instrs | -8 per iter
Stalls | 0 | 0 | —
Flushes | 4 | 4 | —
CPI | 1.059 | 1.082 | —
Output (a) | 0xD576E19B | 0xD576E19B | match
Output (b) | 0x1898E8F8 | 0x1898E8F8 | match
Output (c) | 0x36858953 | 0x36858953 | match
Output (d) | 0x9FF722DF | 0x9FF722DF | match
Real-World Impact
• IoT devices: encrypt sensor data without draining battery
• Secure boot: verify firmware signatures faster at startup
• TLS 1.3: ChaCha20-Poly1305 is the default cipher for mobile
• 26% fewer cycles = proportionally lower energy per packet
Hardware cost: 1 extra ALU case (1 line of Verilog) + 1 opcode decode entry. Minimal area overhead for 1.35x crypto speedup.
VERIFIED: Both software and hardware versions produce identical ciphertext output. Custom ROL is fully compatible with existing pipeline & forwarding.

## Slide 17
CONCLUSION
Summary & Future Work
What We Built
• Complete RV32I processor with 37 + 1 custom instruction
• 5-stage pipeline (IF/ID/EX/MEM/WB) in Verilog
• 9 hardware modules, 675 lines of synthesizable RTL
• Full forwarding unit with 3 bypass paths
• Custom ROL instruction for crypto acceleration
• 5 testbenches with comprehensive verification
Key Results
• CPI = 1.14 on Fibonacci (close to ideal 1.0)
• 4.4x throughput over single-cycle baseline
• 0 data stalls — forwarding handles all RAW hazards
• 87.7% pipeline efficiency
• 1.35x crypto speedup with custom ROL instruction
• 26% cycle reduction on ChaCha20 quarter-round
Key Takeaways
• Forwarding is essential — without it CPI would be 1.6-2.0x
• Branch penalties are the dominant overhead
• Performance counters are critical for analysis
• Custom ISA extensions give measurable speedup
Future Enhancements
• Branch predictor — reduce 2-cycle penalty
• Cache hierarchy — L1 I-cache + D-cache
• RV32M extension — multiply/divide
• More Zbkb crypto ops — ROR, ANDN, pack
• FPGA synthesis — deploy on real hardware
• Full ChaCha20 block — 20 rounds, 256-bit key
Thank You
Adesh Pandey · Aayush Gelal · Bishesh Paudel | Pulchowk Campus · 2026